libShower
Manual
V0.1
As of 28.02.2010
frank.meisel@lhep.unibe.ch

---
Description
- This manual is intended to make the user familiar on the way showers are dealt with.
- The user should not bother about details.
- To increase the performance, the user may give additional information on the date to obtain a better result.

---
Overview
- Shower for Event classification.
- Shower characteristics
- Shower implementation in FEDRA

---
Object description
- A track in fedra
  - One Segment Per Plate
  - N(), Npl(), N0, Theta(), XYZ, P()
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP

---
Object description
- A shower in fedra
  - Can have More than One Segment Per Plate
  - N(), Npl(), N0, Theta(), XYZ, P()
  - Plus additional information: longitudinal&transversal Profile!
Shower
Represented as
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP

---
Object description
- Using EdbTrackP as object class for Shower is ok, but we lose physical information.
- Compensated by infos in EdbShowerAlgE...
    - May be put later in a extra EdbShowerP class...
- Up to now: how is a shower represented/stored?
- We have Shower.root which uses a TTree to store the variables. Technically equivalent to do storage like EdbTrackP, but it requires complex I/O conversions to get from
    - TTree entry ↔ EdbTrackP
Due to backward compabilities we have to use this way.
This is a pain in the back... :-)

---
What is to be done for showers?
- In case we have scanback done, vertex found, scanforth done (hadr. re-interaction), we need for the full description of the event some other information: showers?
- Why are showers for the event classification important?
- Electrons: nu_e from beam; tau->e;
- Photons: present in almost any event, mainly through the decay of:
- Pi0: Find two photons, match them in case of more

---
Finding showers
- Showers are either attached to vertex directly or indirectly:
  - Electrons: start to shower direct from the vertex without flight length; IP to vertex rather small; DeltaZ to vertex very small.
  - Photons: fly – then showering happens; therefore IP to vertex bigger than attached tracks; DeltaZ to vertex can be large (mean flight length ca10plates).
- Finding a electron shower can be easier than photon shower (directly attached track or BT)

---
Properties of Showers
- We need to be sure of the following things.
- We have to find the shower (start)
- We have to reconstruct (collect all the tracks) it having as much of it reconstructed as possibles (lowest loss as possible).
- After shower(s) found and reconstructed we need the main properties:
    - Energy
    - ID
    - 1ry-2ry vtx attachment

---
Properties of showers: the Shower.root file. a) basic quantities
Name in Shower.root
Description
Analogy in EdbTrackP
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I

---
Reconstruction: Mode A
ShowerInstance = new EdbShowerRec();
ShowerInstance-> SetInBTArray(TObjArray* InBTArray);
ShowerInstance-> SetEdbPVRec(EdbPVRec* Ali);
ShowerInstance-> Execute();
ShowerInstance-> GetRecoShowerArray();
- Choose Initiator Basetracks:
- Set the PVR object on which the reconstruction shall operate:
- Start Reconstruction
- Retrieve Reconstructed Shower Array

---
Reconstruction: Mode B
Frederics Algo Implementation
- To be filled and explained...:
- void recdown(int num, int MAXPLATE, int DATA, int Ncand, double* x0, double* y0, double* z0, double* tx0, double* ty0, double* chi20, int* W0, double* P0, int* Flag0, int* plate0, int* id0, int* TRid, double* Esim, int piece2, int piece2par)

---
Shower Energy Measurement
- The Shower Energy is measured using:
    - Basic Properties of the Shower
    - Conditions from Brick Scanning
- Shower Properties
  - Shape
  - Density
  - Angle
- Scan Conditions
  - Reco Efficiency
  - BG Level

---
Block diagram: energy
Shower
Characteristics
Energy class
instance
E= 4.2 +- 1.8 +- 0.5 GeV
Scan cond. Info
==Track->P()
Shower
Represented as
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP

---
Implemented ScanEfficiencies
Example Brick: Bern 144320, Mic4

---
Energy: Technical
- Get Reconstructed Shower Array
- Start Energy Estimation
- Retrieve Reconstructed Shower Array, with P() filled.
        // Instantate ShowerAlgorithmEnergy Class
        EdbShowerAlgESimple* ShowerAlgEnergyInstance = new EdbShowerAlgESimple();
        // Run Shower Energy Algorithm on all shower/tracks
        ShowerAlgEnergyInstance->DoRun(RecoShowerArray);
        // All tracks contain now in P() the estimated energy.

---
Energy: stat. Results: sigma(E)/E
gamma

---
Energy: stat. Results: sigma(E)/E
ele

---
Interpolation
- Interpolate energy statistic uncertanties with ROOT Tspline3 class (between energies)
- (No interpolation done between plate binnings.)

---
More here : SYSTEMATICS
- Calculating energy gives you stat. AND sys. On the screen. Saved is then the quadratic sum.
  - (Attention: at the moment (svn1056) in fedra there is no additional variable to store momentum/energy error of a track/shower. Uncertainty is now only written in shower.root file.)
- Different sources have been investigated.
- See the following table for an overview.
  - (Details will be written up in the thesis, also many plots and tables; explanations will follow here)

---
	DEPENDS ON ENERGY ??	DEPENDS ON NPLATES ??	E/G IMPACT ??	PRIORITY	Sample Resolution/E gamma @ 1GeV@20Pl	Sample Resolution/E Electron @ 4GeV@20Pl
FROM THE SCANNING METHOD
EFFICIENCY MISMATCH	YES	YES	NO	HIGH	0.12	0.16
BG LEVEL	YES	YES	YES	HIGH	?	?
NPL, Before,After match	YES	YES	NO	MIDDLE	0.026	0.081
DISALIGNMENT	YES	YES	NO	(SKIP)	-	-
FROM THE RECO METHOD
E/G MISMATCH	YES	YES	NO	LOW	0.04	0.03
Shower Alg
FROM THE Multivariate METHOD
N TRAININGS CYLCES	YES	YES	NO	LOW	-	-
N TRAININGS EVENTS	YES	YES	NO	LOW	-	-
TYPE TRAININGS FILE	YES	YES	NO	MIDDLE	-	-
Cycles&Events(File fixed)	YES	YES	NO	LOW	0.012	0.0068
FROM THE MONTE CARLO METHOD
QUALITY CUT	-	-	-	LOW	?	?
SHOWER PARAMETRISATION	-	-	-	(SKIP)	-	-
ESTIMATED SUM SYST. / (+linear, i.e. Overestimated a bit)					<0.33	<0.4
STATISTICAL					0.48	0.38

---
E: Systematics
- Show uncertainties from different sources.
- Electrons left, Photons right.
- (Tables with full valueset will be put later)
- Take Care of different Y-axis scaling!

---
E: Systematics: Eff mismatch

---
E: Systematics: NPL mismatch

---
E: Systematics: ID mismatch

---
E: Systematics: ANN uncertainty

---
E: Systematics: Addition
- As we know, systematic sources are neither totally independent nor totally dependent...
- But to derive an analytical form for the covariance elements is even more impossible in experimental cases (no analytical function to describe the dependencies)
- To calculate ALL variations by means of MC estimates would require tooo much computing power.
- So tradeoff here: take the sources listed in table and add them
  - Quadratically:	sigma^sys_tot= QSUM(sigma^sys_i)
  - Linear:	sigma^sys_tot= LSUM(sigma^sys_i)
- „True“ error will be in between....
- The more systematic sources considered, the larger the error we get.
- We think that the most important we have investigated...

---
Shower ID
- Problem:
  - One single Shower can originate from either photons, electrons or (charged) pions
- Solution:
  - Shower ID class, which does a differentiation!
- Technicalities:
  - The ID class determines Shower from its originating particle

---
Shower ID
- Instead of assigning the ANN one number for
    - Gamma, Electron, Pion(+-)
- We do decions based on „X vs Y“, i.e.
    - Gamma vs Electron
    - Electron vs Pion
- Because the ANN is better in discriminating two-by-two variable discrimination.
- In continuation with former implementations, we save these results in eProb1,eProb90_X_vs_Y
Eprob1: bg rejection at 1%
Eprob90: signal efficiency 90%

---
Shower ID
- Two type of variables:
  - SHID: 0(G),1(E),2(P)
  - SPID: 0,1,2
  - So we can assign a unique
  - ID for each combination:
  - Example:
    - gamma_vs_e: SHID=0,SPID=1
    - e_vs_pi: SHID=1,SPID=2
  - Always put	0 if it belongs to Type 0 (SHID)
  - Always put	1 if it belongs to Type 1 (SPID)
G
P
E

---
Block diagram: ID
Shower
Characteristics
ID class
instance
Gamma
Electron
Pion
Vertex Info
==Track->Flag()
Shower
Represented as
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP

---
More here...

---
The Cleaning of High BG level...
- We try to keep a constant BT density level of not more than 40BT/mm2
- To get this, we have the EdbPVRec patterns object, which we use for checks:
- We calculate BT density plate by plate and can adapt the Quality Cut plate by plate accordingly.