libShowRec
Manual
V0.1
frank.meisel@lhep.unibe.ch

---
Description
- This manual is intended to make the user familiar on the way showers are dealt with
- The user should not bother about details of programming
- To increase the performance, the user may give additional information on the date to obtain a better result

---
Overview
- Shower for Event classification.
- Shower characteristics
- Shower implementation in FEDRA

---
EdbShowRec
ShowerRecoModule
PackageManager(EdbShowRec)
EdbShow
Alg_1
Volume
(EdbPVRec)
Algorithms Reco (EdbShowAlg)
ShowerIDModule
ShowerEnergyModule
Tracks
(EdbTrackP)
Showers
(EdbShowerP)
I/O Objects
EdbShow
Alg_3
EdbShow
Alg_2
EdbShow
Alg_ID_1
EdbShow
Alg_ID_2
EdbShow
Alg_E_1
EdbShow
Alg_E_2
Algorithms ID (EdbShowAlg)
Algorithms Reco (EdbShowAlg)
Algorithms Energy (EdbShowAlg)
ShowerIOModule

---
Object description
- A track in fedra
      - One Segment Per Plate
      - N(), Npl(), N0, Theta(), XYZ, P()
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbTrackP

---
Object description
- A shower in fedra
      - Can have More than One Segment Per Plate
      - N(), Npl(), N0, Theta(), XYZ, P()
      - Plus additional information: longitudinal&transversal Profile!
Hole
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbShowerP
EdbSegP
EdbSegP
Hole

---
    Schematic comparison:
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbShowerP
EdbSegP
EdbSegP
Hole

---
Object description
- Using EdbTrackP as object class for Shower is ok, but we lose physical information.
- Compensated by infos in EdbShowerAlgE...
    - May be put later in a extra EdbShowerP class...
- Up to now: how is a shower represented/stored?
- We have Shower.root which uses a TTree to store the variables. Technically equivalent to do storage like EdbTrackP, but it requires complex I/O conversions to get from
    - TTree entry ↔ EdbTrackP
Due to backward compabilities we have to use this way.
This is a pain in the back... :-)

---
What is to be done for showers?
- In case we have scanback done, vertex found, scanforth done (hadr. re-interaction), we need for the full description of the event some other information: showers?
- Why are showers for the event classification important?
- Electrons: nu_e from beam; tau->e;
- Photons: present in almost any event, mainly through the decay of:
- Pi0: Find two photons, match them in case of more

---
Finding showers
- Showers are either attached to vertex directly or indirectly:
  - Electrons: start to shower direct from the vertex without flight length; IP to vertex rather small; DeltaZ to vertex very small.
  - Photons: fly – then showering happens; therefore IP to vertex bigger than attached tracks; DeltaZ to vertex can be large (mean flight length ca10plates).
- Finding a electron shower can be easier than photon shower (directly attached track or BT)

---
Properties of Showers
- We need to be sure of the following things.
- We have to find the shower (start)
- We have to reconstruct (collect all the tracks) it having as much of it reconstructed as possibles (lowest loss as possible).
- After shower(s) found and reconstructed we need the main properties:
    - Energy
    - ID
    - 1ry-2ry vtx attachment

---
Properties of the Shower.root file. a) basic quantities
Name in Shower.root
Description
Analogy in EdbTrackP
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I
Number of Basetracks
Plate ID of BT[i]
Number of Plates Crossed
X,Y,Z Coordinates of BT[i]
TX,TY Coordinates of BT[i]
??(to be looked up)
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
MC event number
N()
??(to be looked up)
Npl()
->X(),Y(),Z()
->TX(),TY()
??(to be looked up)
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
->MCEvt()

---
Properties of the Shower.root file. b) derived quantities
Name in Shower.root
Description
Analogy in EdbTrackP
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I
sizeb
nfilmb[]
lengthfilmb
x,y,z	-b[]
tx,ty	-b[]
plateb	-b[]
Numbereventb[]
showerID/I
isizeb/I
ntrace1simu[sizeb]/I
ntrace2simu[sizeb]/I
ntrace3simu[sizeb]/I
Ntrace4simu[sizeb]/I
chi2btkb[sizeb]/F
number_eventb/I

---
Reconstruction: Mode A
ShowerInstance = new EdbShowerRec();
ShowerInstance-> SetInBTArray(TObjArray* InBTArray);
ShowerInstance-> SetEdbPVRec(EdbPVRec* Ali);
ShowerInstance-> Execute();
ShowerInstance-> GetRecoShowerArray();
- Choose Initiator Basetracks:
- Set the PVR object on which the reconstruction shall operate:
- Start Reconstruction
- Retrieve Reconstructed Shower Array

---
Reconstruction: Mode B
Frederics Algo Implementation
- To be filled and explained...:
- void recdown(int num, int MAXPLATE, int DATA, int Ncand, double* x0, double* y0, double* z0, double* tx0, double* ty0, double* chi20, int* W0, double* P0, int* Flag0, int* plate0, int* id0, int* TRid, double* Esim, int piece2, int piece2par)

---
Shower Reconstruction Algorithms
- There have been tested several algorithms to find out optimal shower reconstruction.
- Some are similar to each other, some are different.
- They can be grouped into two types:
    - Local Basetrack Cut Algorithms (CT, CA, OI, RC, BW)
    - Global Basetrack Cut Algorithms (CL, TC, GS)
- Pseudocodes of all algorithms can be found in thesis, code for OI and GS algo are given in next two slides:

---
Shower Reco Alg: OI

---
Results for Shower Reco Algs:
OI
GS

---
Shower Energy Measurement
See extra file...

---
Shower ID
- Problem:
  - One single Shower can originate from either photons, electrons or (charged) pions
- Solution:
  - Shower ID class, which does a differentiation!
- Technicalities:
  - The ID class determines Shower from its originating particle

---
Shower ID
- Instead of assigning the ANN one number for
    - Gamma, Electron, Pion(+-)
- We do decions based on „X vs Y“, i.e.
    - Gamma vs Electron
    - Electron vs Pion
- Because the ANN is better in discriminating two-by-two variable discrimination.
- In continuation with former implementations, we save these results in eProb1,eProb90_X_vs_Y
Eprob1: bg rejection at 1%
Eprob90: signal efficiency 90%

---
Shower ID
- Two type of variables:
  - SHID: 0(G),1(E),2(P)
  - SPID: 0,1,2
  - So we can assign a unique
  - ID for each combination:
  - Example:
    - gamma_vs_e: SHID=0,SPID=1
    - e_vs_pi: SHID=1,SPID=2
  - Always put	0 if it belongs to Type 0 (SHID)
  - Always put	1 if it belongs to Type 1 (SPID)
G
P
E

---
Block diagram: ID
Shower
Characteristics
ID class
instance
Gamma
Electron
Pion
Vertex Info
==Track->Flag()
Shower
Represented as
EdbTrackP
EdbSegP
EdbSegP
EdbSegP
Hole
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP
EdbSegP

---
More here...

---
The Cleaning of High BG level...
- We try to keep a constant BT density level of not more than 40BT/mm2
- To get this, we have the EdbPVRec patterns object, which we use for checks:
- We calculate BT density plate by plate and can adapt the Quality Cut plate by plate accordingly.

---
EdbPVRQuality
- This class does BG cleaning... How it works:
- EdbPVRQuality* Qualityobject = new EdbPVRQuality(gAli);
    - gAli is the filled EdbPVRec object. Usually this implicates the data coming from cp.root files.
    - LinkedTracks.root EdbPVRec object usually is already very „clean“, i.e. that linked tracks are often „good“ (physically) objects.
- Qualityobject->Print();
- Qualityobject->Help();

---
EdbPVRQuality Remove FakeDoublets.
- From Scanning we know that by view overlap of the microscope there is fake double Bts:
  - One BT scanned in two views appears (due to Sysal bending correction function) as two slightly shifted different Bts!
  - This we dont want, since several reasons. One of them is for the GammaPairSearch: The pair algo might take these as a e+e—Pair.
- Those duplicated tracks show a distinct behaviour in the dR-dT plane.
- Plot: photon pairs and instrumental BG doublets in ther dR-dT plane
- EdbPVRQuality* Qualityobject = new EdbPVRQuality(gAli);
- Qualityobject->Remove_DoubleBT();
- Returns a new EdbPVRec Object, where these doublets are eliminated.

---
Zoom on very small
dR-dT difference values:
What are these line parings???
Still unknown...

---
InBT - Execution order
EdbShowerRec
In general:
Look:
Check: plates,
        Track..
OK?
EdbPVRec
In Object ???
YES
Check: linked_tracks
in PVR-object?
eTracks
Check: linked_tracks
in PVR/object/file?
Use eAli
NO
STOP
In File ???
YES
NO
Check: vertices in
PVR-object/file?
eVertices
Use eTracks
STOP
YES
Use eVertices
Use: eAli as source
Use: eTrack, eVertices to fill InBT
---------------------------------------------
START RECO
Optimal Case.
NO
NO
NO

---
BG - Execution order
EdbShowerRec
Check: Global
Basetrack
 Density
OK?
EdbPVRec
YES
Check: linked_tracks
in PVR-object?
eTracks
Check: linked_tracks
in PVR-object/file?
For passing sub-
straction.
Use eAli
YES
Check: vertices in
PVR-object?
eVertices
Use eTracks
YES
Use eVertices
Optimal Case.
Use: Constant QualityCut
Use: Passing Track Substraction, Double BT substraction.
-------------------------------------------------------------
SET NEW EdbPVRec FOR RECONSTRUCTION
YES
NO
NO

---
How the Initiator Basetracks are selected.
Default Configuration.
EdbShowerRec
Scanned Volume
(EdbPVRec)
Tracks
(eTracks)
Vertices
(eVertices)
YES
NO
Exit shower
reconstruction
YES
NO
YES
NO
Use all segments of
the volume
Use first segment
of the tracks
YES
NO
Use segments with
IP<250 mm to vertex
YES

---
Global basetrack
density ok?
Do nothing. Use
unchanged volume.
Add passing track
substraction.
Linked tracks
exist?
Execute constant
density method.
Execute constant
quality method.
Cleaned Volume
(EdbPVRec)
How the background cleaning is done.
Default Configuration.
Scanned Volume
(EdbPVRec)
NO
YES
NO
YES