Comments on testbeam setup
At CERN we can have e/pi beam with well defined energy, fair known coposition and fair known intensity.
Goal of TestBeam exposure: to validate electron reconstruction and energy measurement for opera case.

---
- We had an exposure of 4 testbeam bricks in Sep.2009: 1,3,3,4GeV.
- Four or five beam bunches had been shot onto each brick (straight+1angle).
- Afterwards no additional cosmic exposure.
- Analyzing the bricks is not yet fully finished.
- First results of the analysis:
  - ...
Sorry, not enough time to grab the old plots I made long time ago....

---
Prelim Result Statements
- Data Quality is rather good.
  - Scanning smooth.
  - Purity of sample ok.
  - Nor grey or black emulsions.
- Alignment can/must be done with pions from the beam.
  - Bricks were stored horizontally during car/stay, that incoming cosmics are at 90degree to emulsion.

---
- Momentum Measurement of pions:
  - Reproducable all 4 momentum mean values.
  - Errors (Gaus/RMS) on p are higher than in the note:
      - Scanning impurities, garbage, emulsion displacement.

---
- Energy Measurement of electrons:
  - Bricks have a relatively high density of electrons next to each other, the mean distance to another electron is about 600 micron. The standard ConeTube OPERA reco is 800 tube diameter.
  - Overlapping occurs for many showers, i.e. Internal impurities!
  - First estimation: after 10 plates, about 30% overlap (in simulation)
  - Solution methods: tighten reco cut criteria.
      - Appropriate for TB data, Inaproriate for Opera events, large loss of shower collection efficiency!

---
Recommendations
for a new TB setup.
- The TB has to reflect the standard Opera case as close as possible:
  - Take full Brick, including CS; put in in beamline same way as in Opera (i.e. CS at end of the beam).
  - Avoid shower overlaps, i.e. reduce number of beam bunches. It is better to scan larger areas for longer time, than instead introducing new systematic biases.
  - Use the average electron incoming angle rather than straigt electrons.
  - For nu_e and tau case focus on more energetic values (not 1GeV).